## Slide 1
Attack Surface Cards (Front)
1. Ecosystem Access Control
Vulnerability
- Interoperability standards
- Data governance
- System wide failure
- Individual stakeholder risks
- Implicit trust between components
- Enrollment security
- Decommissioning system
- Lost access procedures
Information gathered with the device by constructing the ecosystem can be used for big data analysis etc.
2. Device Memory
Vulnerability
- Sensitive data
- Cleartext usernames
- Cleartext passwords
- Third-party credentials
- Encryption keys
Devices have memory for temporarily holding information obtained from the sensor.
3. Device Physical Interfaces
Vulnerability
- Firmware extraction
- User CLI
- Admin CLI
- Privilege escalation
- Reset to insecure state
- Removal of storage media
- Tamper resistance
- Debug port
- UART (Serial), JTAG / SWD
- Device ID number exposure
Devices have physical interfaces that allows external devices to be connected for collecting information and so on.
4. Device Web Interface
Vulnerability
- Standard set of web application vulnerabilities
- Credential management vulnerabilities:
- Username enumeration
- Weak passwords
- Account lockout
- Known default credentials
- Insecure password recovery mechanism
A web interface is held for viewing device information via the network.
5. Device Firmware
Vulnerability
- Sensitive data exposure
- Hardcoded credentials
- Encryption keys, etc.
- Firmware version display and/or last update date
- Vulnerable services (ssh, tftp, etc.) - Security related function API exposure
- Firmware downgrade possibility
The built-in software recorded of the ROM or the flash memory in the device is held to control the device.
6. Device Network Services
Vulnerability
- Information disclosure
- User or Administrative CLI
- Injection
- Denial of Service
- Unencrypted Services
- Poorly implemented encryption
- Test/Development Services
- Buffer Overflow
- UPnP
- Vulnerable UDP, etc.
Services via the network provided to the user is held for improving their operability.
7. Administrative Interface
Vulnerability
- SQL injection
- Cross-site scripting
- Cross-site Request Forgery
- Username enumeration
- Weak passwords
- Account lockout
- Known default credentials
- Security/encryption options
- Logging options
- Inability to wipe device, etc.
Administrative Interfaces are held for maintaining devices directly or remotely.
8. Local Data Storage
Vulnerability
- Unencrypted data
- Data encrypted with discovered keys
- Lack of data integrity checks
- Use of static same enc/dec key
Device have a local data storage for storing past sensor information, etc.

## Slide 2
Attack Surface Cards (Back)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)

## Slide 3
Attack Surface Cards (Front)
9. Cloud Web Interface
Vulnerability
- Standard set of web application vulnerabilities
- SQL injection, etc.
- Credential management vulnerabilities:
- Username enumeration
- Weak passwords
- Known default credentials, etc.
- Transport encryption
- Two-factor authentication
Cloud web interfaces are held for browsing information transmitted from the device to the cloud.
10. Third-party Backend APIs
Vulnerability
- Unencrypted PII sent
- Encrypted PII sent
- Device information leaked
- Location leaked
Third party backend APIs are used to perform processing, storage, output of results, etc. of information input from the device.
11. Update Mechanism
Vulnerability
- Update sent without encryption
- Updates not signed
- Update location writable
- Update verification
- Update authentication
- Malicious update
- Missing update mechanism
- No manual update mechanism
Updating mechanisms are held to correct device vulnerability etc.
12. Mobile Application
Vulnerability
- Implicitly trusted by device or cloud
- Username enumeration
- Account lockout
- Known default credentials
- Weak passwords
- Insecure data storage
- Transport encryption
- Insecure password recovery mechanism
- Two-factor authentication
Mobile application is used to manage devices from smartphones and tablet terminals and view sensor information.
13. Vendor Backend APIs
Vulnerability
- Inherent trust of cloud or mobile application
- Weak authentication
- Weak access controls
- Injection attacks
- Hidden services
Vendor backend APIs are used to perform data processing, storage, output of results, etc. of information input from the device.
14. Ecosystem Communication
Vulnerability
- Health checks
- Heartbeats
- Ecosystem commands
- Deprovisioning
- Pushing updates
Ecosystem communication is used to realize device status monitoring, etc.
15. Network Traffic
Vulnerability
- LAN
- LAN to Internet
- Short range
- Non-standard
- Wireless (WiFi, Z-wave, XBee, Zigbee, Bluetooth, LoRA)
- Protocol fuzzing
Various network communications are held in order to realize bidirectional communication to devices and gateways.
16. Authentication/Authorization
Vulnerability
- Authentication/Authorization related values (session key, token, cookie, etc.) disclosure
- Reusing of session key, token, etc.
- Device to device authentication
- Device to mobile Application authentication
- Lack of dynamic authentication
Authentication / authorization function is retained to guarantee the exchange of information with legitimate users and devices.

## Slide 4
Attack Surface Cards (Back)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)

## Slide 5
Attack Surface Cards (Front)
17. Privacy
Vulnerability
- User data disclosure
- User/device location disclosure
- Differential privacy
The user's privacy information is stored in the information acquired by devices and the information held by the devices.
18. Hardware (Sensors)
Vulnerability
- Sensing Environment Manipulation
- Tampering (Physically)
- Damage (Physically)
It may be possible to physically access and operate the sensors and its surrounding environment.

## Slide 6
Attack Surface Cards (Back)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)
Attack Surface
(OWASP)