## Slide 1
Counter Measure Cards（Front）
GP-TM-01
Hardware security
THREAT GROUPS
- Physical attacks
- Disasters, - Outages
Employ a hardware-based immutable root of trust. The Hardware Root of Trust is a trusted hardware component which receives control at power-on.
Use hardware that incorporates security features to strengthen the protection and integrity of the device.
- Random Number Generation
- Tamper detection
- TEE (Trusted Execution Environment）
…
GP-TM-02
Hardware security
THREAT GROUPS
- Physical attacks
- Disasters, - Outages
GP-TM-03 Trust and Integrity Management
The boot process initializes the main hardware components, and starts the operating system.
THREAT GROUPS
- Failures / Malfunctions
- Nefarious Activity / Abuse
- Outages
Sign code cryptographically to ensure it has not been tampered with after being signed as safe for the device, and implement run-time protection and secure execution monitoring to be sure malicious attacks do not overwrite code after it is loaded.
GP-TM-04 Trust and Integrity Management
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception / Hijacking
Control the installation of software on operational systems, to prevent unauthenticated software and files being loaded onto it.
GP-TM-05 Trust and Integrity Management
THREAT GROUPS
- Outages, -Nefarious Activity / Abuse - Eavesdropping / Interception / Hijacking
Restore Secure State - Enable a system to return to a state that was known to be secure, after a security breach has occurred or if an upgrade has not been successful.
GP-TM-06 Trust and Integrity Management
THREAT GROUPS
- Outages, -Nefarious Activity / Abuse - Eavesdropping / Interception / Hijacking
Use protocols and mechanisms able to represent and manage trust and trust relationships.
Each communication channel must be trustworthy to a level commensurate with the security dependencies it supports.
GP-TM-07 Trust and Integrity Management
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception / Hijacking
GP-TM-08 Strong default security and privacy
Enable security by default. Any applicable security features should be enabled by default, and any unused or insecure functionalities should be disabled by default.
THREAT GROUPS
- Outages
- Nefarious Activity / Abuse
- Failures / Malfunctions

## Slide 2
Counter Measure Cards（Back）
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)

## Slide 3
Counter Measure Cards（Front）
Establish hard to crack device individual default passwords. And a hard to crack default password is still a weakness if it is used for more than one device.
GP-TM-09 Strong default security and privacy
THREAT GROUPS
- Outages
- Nefarious Activity / Abuse
- Failures / Malfunctions
GP-TM-10
Data protection and compliance
Personal data must be collected and processed fairly and lawfully. The fairness principle specifically requires that personal data should never be collected and processed without the data subject’s consent.
THREAT GROUPS
- Damage / loss (IT Assets)
- Nefarious Activity / Abuse
Make sure that personal data is used for the specified purposes for which they were collected, and that any further processing of personal data is compatible and that the data subjects are well informed.
GP-TM-11
Data protection and compliance
THREAT GROUPS
- Damage / loss (IT Assets)
- Nefarious Activity / Abuse
Minimize the data collected and retained.
Stakeholders must delete raw data as soon as they have extracted the data required for their data processing.
GP-TM-12
Data protection and compliance
THREAT GROUPS
- Damage / loss (IT Assets)
IoT stakeholders must be compliant with the EU General Data Protection Regulation (GDPR).
GP-TM-13
Data protection and compliance
THREAT GROUPS
- Damage / loss (IT Assets)
- Nefarious Activity / Abuse
Users of IoT products and services must be able to exercise their rights to information, access, erasure, rectification, data portability, restriction of processing, objection to processing, and their right not to be evaluated on the basis of automated processing.
GP-TM-14
Data protection and compliance
THREAT GROUPS
- Damage / loss (IT Assets)
- Nefarious Activity / Abuse
GP-TM-15
System safety and reliability
Design with system and operational disruption in mind. Build IoT devices to fail safely and securely, so that the failure does not lead to a greater systemic disruption.
THREAT GROUPS
- Outages - Failures / Malfunctions
- Disasters
Mechanisms for self-diagnosis and self-repair/healing to recover from failure, malfunction or a compromised state.
GP-TM-16
System safety and reliability
THREAT GROUPS
- Failures / Malfunctions
- Outages

## Slide 4
Counter Measure Cards（Back）
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)

## Slide 5
Counter Measure Cards（Front）
Ensure standalone operation - essential features should continue to work with a loss of communications and chronicle negative impacts from compromised devices or cloud-based systems.
GP-TM-17
System safety and reliability
THREAT GROUPS
- Failures / Malfunctions
- Outages
GP-TM-18 Secure Software / Firmware updates
Ensure the device software /firmware, its configuration and its applications have the ability to update Over-The-Air (OTA), that the update server is secure, that the update file is transmitted via a secure connection, that it does not contain sensitive data (e.g. hardcoded credentials)…
THREAT GROUPS
- Outages - Failures / Malfunctions
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Offer an automatic firmware update mechanism. Devices should be configured to check for the existence of firmware updates at frequent intervals. Automatic firmware updates should be enabled by default.
GP-TM-19 Secure Software / Firmware updates
THREAT GROUPS
- Failures / Malfunctions
- Outages
Backward compatibility of firmware updates. Automatic firmware updates should not change network protocol interfaces in any way that is incompatible with previous versions. Users should have the ability to approve, authorize or reject updates.
GP-TM-20 Secure Software / Firmware updates
THREAT GROUPS
- Failures / Malfunctions
- Outages
GP-TM-21
Authentication
Design the authentication and authorization schemes based on the system-level threat models. Devices should include mechanisms to reliably authenticate their backend services and supporting applications.
THREAT GROUPS
- Failures / Malfunctions
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Ensure default passwords and even default usernames are changed during the initial setup, and that weak, null or blank passwords are not allowed.
GP-TM-22
Authentication
THREAT GROUPS
- Failures / Malfunctions
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Authentication mechanisms must use strong passwords or personal identification numbers (PINs), and should consider using multi-factor authentication (MFA) like Smartphones, Biometrics, etc., and certificates.
GP-TM-23
Authentication
THREAT GROUPS
- Failures / Malfunctions
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Authentication credentials including but not limited to user passwords shall be salted, hashed and/or encrypted.
GP-TM-24
Authentication
THREAT GROUPS
- Failures / Malfunctions
- Nefarious Activity / Abuse
- Eavesdropping / Interception

## Slide 6
Counter Measure Cards（Back）
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)

## Slide 7
Counter Measure Cards（Front）
Protect against ‘brute force’ and/or other abusive login attempts by locking or disabling user and device support account(s) after a reasonable number of invalid log in attempts, or making the user wait a certain amount of time to login again after a failed attempt.
GP-TM-25
Authentication
THREAT GROUPS
- Failures / Malfunctions
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Ensure password recovery or reset mechanism is robust and does not supply an attacker with information indicating a valid account. The same applies to key update and recovery mechanisms.
GP-TM-26
Authentication
THREAT GROUPS
- Failures / Malfunctions
- Nefarious Activity / Abuse
- Eavesdropping / Interception
GP-TM-27
Authorisation
Limit permissions of the allowed actions for a given system (e.g., the information owner or the database administrator determines who can update a shared file accessed by a group of online users).
THREAT GROUPS
- Failures / Malfunctions
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Device firmware should be designed to isolate privileged code, processes and data from portions of the firmware that do not need access to them, and device hardware should provide isolation concepts to prevent unprivileged from accessing security sensitive code.
GP-TM-28
Authorisation
THREAT GROUPS
- Failures / Malfunctions
- Nefarious Activity / Abuse
- Eavesdropping / Interception
GP-TM-29
Access Control - Physical and Environmental security
Data integrity and confidentiality must be enforced by access controls. When the subject requesting access has been authorised to access particular processes, it is necessary to enforce the defined security policy.
THREAT GROUPS
- Physical Attacks - Malfunctions
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Ensure a context-based security and privacy that reflects different levels of importance (e.g. emergency crisis, home automation).
GP-TM-30
Access Control - Physical and Environmental security
THREAT GROUPS
- Malfunctions - Nefarious Activity - Eavesdropping / Interception
- Damage / Loss (IT Assets)
Since some devices, gateways, etc. are required to be managed remotely rather than operated manually in the field, measures for tamper protection and detection are needed. Detection and reaction to hardware tampering should not rely on network connectivity.
GP-TM-31
Access Control - Physical and Environmental security
THREAT GROUPS
- Physical attacks
- Nefarious Activity / Abuse
Ensure that the device cannot be easily disassembled and that the data storage medium is encrypted at rest and cannot be easily removed.
GP-TM-32
Access Control - Physical and Environmental security
THREAT GROUPS
- Physical attacks
- Nefarious Activity / Abuse

## Slide 8
Counter Measure Cards（Back）
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)

## Slide 9
Counter Measure Cards（Front）
Ensure that devices only feature the essential physical external ports (such as USB) necessary for them to function and that the test/debug modes are secure, so they cannot be used to maliciously access the devices. In general, lock down physical ports to only trusted connections.
GP-TM-33
Access Control - Physical and Environmental security
THREAT GROUPS
- Physical attacks
- Eavesdropping / Interception /
- Failures / Malfunctions
Ensure a proper and effective use of cryptography to protect the confidentiality, authenticity and/or integrity of data and information, in transit and in rest. Ensure the proper selection of standard and strong encryption algorithms and strong keys, and disable insecure protocols.
GP-TM-34
Cryptography
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Cryptographic keys must be securely managed.
Cryptographic key management includes key generation, distribution, storage, and maintenance.
GP-TM-35
Cryptography
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Build devices to be compatible with lightweight encryption and security techniques that can, on the one hand, be usable on resource-constrained devices, and, on the other hand, be scalable so to minimise the management effort and maximise their usability.
GP-TM-36
Cryptography
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Support scalable key management schemes. It has to be considered that tiny sensor nodes cannot provide all security features because they have lots of system limitations.
GP-TM-37
Cryptography
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception
- Failures / Malfunctions
Guarantee the different security aspects of the information in transit on the networks or stored in the IoT application or in the Cloud, using data encryption methods to minimise network threats such as replay, interception, packet sniffing, wiretapping, or eavesdropping.
GP-TM-38 Secure and trusted communications
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception
- Failures / Malfunctions
Ensure that communication security is provided using state-of-the-art, standardised security protocols, such as TLS for encryption.
GP-TM-39 Secure and trusted communications
THREAT GROUPS
- Eavesdropping / Interception
- Damage / Loss (IT Assets)
Ensure credentials are not exposed in internal or external network traffic
GP-TM-40 Secure and trusted communications
THREAT GROUPS
- Eavesdropping / Interception
- Damage / Loss (IT Assets)

## Slide 10
Counter Measure Cards（Back）
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)

## Slide 11
Counter Measure Cards（Front）
Guarantee data authenticity to enable trustable exchanges (from data emission to data reception - both ways). Data is often stored, cached, and processed by several nodes; not just sent from point A to point B.
GP-TM-41 Secure and trusted communications
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Do not trust data received and always verify any interconnections.
Discover, identify and verify/authenticate the devices connected to the network before trust can be established, and preserve their integrity for trustable solutions and services.
GP-TM-42 Secure and trusted communications
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception
- Failures / Malfunctions
IoT devices should be restrictive rather than permissive in communicating: When possible, devices should not be reachable via inbound connections by default.
GP-TM-43 Secure and trusted communications
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Prevent unauthorised connections to it or other devices the product is connected to, at all levels of the protocols. IoT devices must provide notice and/or request a user confirmation when initially connecting with other devices, platforms or services.
GP-TM-44 Secure and trusted communications
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Disable specific ports and/or network connections for selective connectivity. If necessary, provide users with guidelines to perform this process in the final implementation.
GP-TM-45 Secure and trusted communications
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Rate limiting – controlling the traffic sent or received by a network to reduce the risk of automated attacks.
GP-TM-46 Secure and trusted communications
THREAT GROUPS
- Nefarious Activity / Abuse
- Eavesdropping / Interception
Risk Segmentation - Splitting network elements into separate components to help isolate security breaches and minimise overall risk. Networks can be divided into isolated subnetworks to boost performance and improve security.
GP-TM-47 Secure Interfaces and network services
THREAT GROUPS
- Eavesdropping / Interception
Protocols should be designed to ensure that, if a single device is compromised, it does not affect the whole set, since smart objects are often deployed as sets of identical or almost identical devices.
GP-TM-48 Secure Interfaces and network services
THREAT GROUPS
- Eavesdropping / Interception

## Slide 12
Counter Measure Cards（Back）
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)

## Slide 13
Counter Measure Cards（Front）
Avoid provisioning the same secret key in an entire product family, since compromising a single device would be enough to expose the rest of the product family.
GP-TM-49 Secure Interfaces and network services
THREAT GROUPS
- Eavesdropping / Interception
Ensure only necessary ports are exposed and available.
GP-TM-50 Secure Interfaces and network services
THREAT GROUPS
- Failures / Malfunctions
- Eavesdropping / Interception
Implement a DDoS-resistant and Load-Balancing infrastructure to protect the services against DDoS attacks which can affect the device itself or other devices and/or users on the local network or other networks.
GP-TM-51 Secure Interfaces and network services
THREAT GROUPS
- Nefarious Activity / Abuse
Ensure web interfaces fully encrypt the user session, from the device to the backend services, and that they are not susceptible to XSS, CSRF, SQL injection, etc.
GP-TM-52 Secure Interfaces and network services
THREAT GROUPS
- Nefarious Activity / Abuse
Avoid security issues when designing error messages. An error message should give/display only the concise information the user needs – it must not expose sensitive information that can be exploited by an attacker, such as an error ID, the web server's version, etc.
GP-TM-53 Secure Interfaces and network services
THREAT GROUPS
- Nefarious Activity / Abuse
Data input validation (ensuring that data is safe prior to use) and output filtering.
GP-TM-54 Secure input and output handling
THREAT GROUPS
- Failures / Malfunctions
- Nefarious Activity / Abuse
Implement a logging system that records events relating to user authentication, management of accounts and access rights, modifications to security rules, and the functioning of the system. The logs must also be preserved on durable storage and retrievable via an authenticated connection.
GP-TM-55
Logging
THREAT GROUPS
- Damage / Loss (IT Assets)
Implement regular monitoring to verify the device behavior, to detect malware and to discover integrity errors.
GP-TM-56
Monitoring and Auditing
THREAT GROUPS
- Damage / Loss (IT Assets)

## Slide 14
Counter Measure Cards（Back）
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)

## Slide 15
Counter Measure Cards（Front）
The auditing of security-relevant events and the monitoring and tracking of system abnormalities are key elements in the after-the-fact detection of, and recovery from, security breaches. Conduct periodic audits and reviews of security controls to ensure that the controls are effective.
GP-TM-57
Monitoring and Auditing
THREAT GROUPS
- Damage / Loss (IT Assets)
- Nefarious Activity / Abuse
Developers should prepare and communicate a product sunset plan from the initial stages to ensure that manufacturers and consumers are aware of the risks posed to a device beyond its expected expiry date.
GP-OP-01
End-of-life support
THREAT GROUPS
- Failures / Malfunctions
Disclose the duration and end-of-life security and patch support (beyond product warranty). Such disclosures should be aligned to the expected lifespan of the device and communicated to the consumer prior to purchase.
GP-OP-02
End-of-life support
THREAT GROUPS
- Failures / Malfunctions
Monitor the performance and patch known vulnerabilities up until the “end-of-support” period of of a product’s lifecycle.
GP-OP-03
End-of-life support
THREAT GROUPS
- Damage / Loss (IT Assets)
- Nefarious Activity / Abuse
- Failures / Malfunctions
Use proven solutions, i.e. well known communications protocols and cryptographic algorithms, recognized by the scientific community, etc. Certain proprietary solutions, such as custom cryptographic algorithms, should be avoided.
GP-OP-04
Proven solutions
THREAT GROUPS
- Damage / Loss (IT Assets)
- Nefarious Activity / Abuse
Establish procedures for analysing and handling security incidents. Establish management procedures in order to ensure a quick, effective and orderly response to information security incidents.
GP-OP-05
Management of security vulnerabilities and/or incidents
THREAT GROUPS
- Damage / Loss (IT Assets)
- Failures / Malfunctions
Coordinated disclosure of vulnerabilities, including associated security practices to address identified vulnerabilities. A coordinated disclosure policy should involve developers, manufacturers, and service providers.
GP-OP-06
Management of security vulnerabilities and/or incidents
THREAT GROUPS
- Damage / Loss (IT Assets)
- Abuse - Eavesdropping
- Outages - Failures / Malfunctions
Participate in information sharing platforms to report vulnerabilities and receive timely and critical information about current cyber threats and vulnerabilities from public and private partners.
GP-OP-07
Management of security vulnerabilities and/or incidents
THREAT GROUPS
- Damage / Loss (IT Assets)

## Slide 16
Counter Measure Cards（Back）
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)

## Slide 17
Counter Measure Cards（Front）
Create a publicly disclosed mechanism for vulnerability reports. Bug Bounty programs, for example, rely on crowdsourcing methods to identify vulnerabilities that companies’ own internal security teams may not catch.
GP-OP-08
Management of security vulnerabilities and/or incidents
THREAT GROUPS
- Damage / Loss (IT Assets)
Ensure the personnel practices promote privacy and security - train employees in good privacy and security practices for the secure usage of the systems, recognizing that technological expertise does not necessarily equate to security expertise.
GP-OP-09
Human Resource Security Training and Awareness
THREAT GROUPS
- Nefarious Activity / Abuse
Document and monitor the privacy and security training activities.
GP-OP-10
Human Resource Security Training and Awareness
THREAT GROUPS
- Nefarious Activity / Abuse
Ensure that cybersecurity roles and responsibilities for all workforce are established and introduce personnel assignments in accordance with the specifics of the projects and security engineering needs.
GP-OP-11
Human Resource Security Training and Awareness
THREAT GROUPS
- Nefarious Activity / Abuse
Data processed by a third-party (i.e., if the organisation utilises a cloud email provider), must be protected by a data processing agreement with the third-party.
GP-OP-12
Third-Party relationships
THREAT GROUPS
- Failures / Malfunctions
Only share consumers’ personal data with third parties with consumers’ affirmative consent, unless required and limited for the use of product features or service operation.
GP-OP-13
Third-Party relationships
THREAT GROUPS
- Failures / Malfunctions
- Damage / Loss (IT Assets)
For IoT hardware manufacturers and IoT software developers it is necessary to adopt cyber supply chain risk management policies and to communicate cyber security requirements to its suppliers and partners.
GP-OP-14
Third-Party relationships
THREAT GROUPS
- Failures - Damage / Loss (IT Assets) - Abuse - Eavesdropping / Interception - Outages

## Slide 18
Counter Measure Cards（Back）
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)
Countermeasure
(ENISA)